SYSTEMS

ARROW PA-28R-200 N5083S (S/N 7135082)

0.

SPEEDS MPH							FLAPS

Vso		64						Plain Manual Extension 10°, 25°, 40°

Vs		70

Vx		81 gear down 91 gear up				WEIGHT AND BALANCE

Vy		85 gear down 95 gear up				Gross Weight 	2600 lbs

Va		134						Baggage Max	200 lbs

Vfe		125

Vle		150						N5083S

Vlo retract		125						Basic Empty	1547.13

Vlo extend		150						Moment		132273.663

Vno		170						Arm		85.496”

Vne		214						Useful load 1052.87     	Payload (full fuel)	765

Best Glide		105

Vr		65						DE-ICE							   							Pitot heat, Windshield defrost

Short Field T/O

Vr		60						HEATER

25° flaps								Shroud surrounding muffler

Enroute Climb	110						PROPELLER

Hartzell 72.5”-74” 2 bladed, constant speed, all metal, controllable pitch

NORMAL APPROACH

Downwind 15”-17” MP 115MPH 10°Flaps					FUEL

Base	 14” MP 105 MPH 25° Flaps					50 gals total, 48 usable, 25 gals each side

Final	 12”-14” MP 90 MPH 40° Flaps					10 GPH approximate

100LL blue, 100/130

ELECTRICAL

12 volt DC system

MAX DEMONSTRATED X-WIND COMPONENT				14 volt, 60 amp alternator

20 MPH (17 KTS)							12 volt battery located aft of baggage compartment

LOAD FACTOR							GEAR

+3.8 G’s Max – Normal Category					Retractable tricycle type

Inverted and acrobatic maneuvers prohibited					Hydraulically actuated electrically driven reversible pump

Power pack (electric motor and hydraulic pump) located aft of bulkhead

ENGINE								Auto gear extension has been disabled

Lycoming IO-360-C1C						9 gear micro switches include…

200 HP 2700 RPM @ Sea Level on a standard day				- 3 greens OFF gear up or in transit

4 cylinder direct drive, horizontally opposed, fuel injected, air cooled		- 3 greens gear down and locked

- 1 squat switch (left main)

OIL 								- throttle horn (gear up below 14” MP)

8 QTS Max 2 QTS Min						- flap horn (beyond 10° Flaps w/gear up)

Operating range 6-8 qts

SAE 50 above 60°F

SAE 40 30°-90°F

SAE 30 0°-70°F

SAE 20 below 10°F

More Oil Pressure = High Pitch Low RPM (cruise)			Less Oil Pressure = Low Pitch High RPM (takeoff)