Cessna 152

V Speeds

Vso…………………...35 kts

Vs..…………………...40 kts

Vr…………………….50 kts

Vx…………………....55 kts

Vy……………………67 kts

Vfe…………………...85 kts

Va……………………104 kts @ 1670

93 kts @ 1350

Vno…………………..111 kts

Vne…………………..149 kts

Best glide…………….60

Normal Approach……60-70

Cruse Climb………….80 kts

Max Window Open….149 kts

Max Demo X-Wind…12 kts

Normal T/O - Rotate at 50 KIAS

Short Field T/O

Lift off at 50 KIAS

Flaps 10 degrees

Normal approach

30 deg flaps : 65 kts

0 flaps          : 70 kts

Flaps Limitations

Takeoff:  0⁰ - 10⁰

Landing: 0⁰ - 30⁰

Weights

Maximum Ramp Weight:  1675 lbs.

Maximum Takeoff Weight:  1670 lbs.

Maximum Landing Weight:  1670 lbs.

Basic Empty Weight:  1191.55 lbs.

Maximum Baggage Weight: 120 lbs.

Area 1:  120 lbs.

Area 2:  40 lbs.

Engine	Lycoming O-235-L2C

110 hp @ 2550RPM

4 cylinders

Direct Drive

Horizontally opposed

Air Cooled

Propeller	McCauley 1A103

Two Blades

Fixed Pitch

Diameter

Minimum:  67.5 in.

Maximum: 69 in.

Fuel		Gravity Fed

100LL blue

Full Tanks

37.5 Gal Useable

(1.5 Unusable)

Filled @ Tabs

24.5 Gal Useable

(1.5 Unusable)

6 g.p.h. average fuel burn

Electrical	28 volt DC system

28 volt 60 amp alternator

24 volt 35 AMP battery

Oil		6 qts max

4 qts min

Winter: Ashless 30W65

Summer: Ashless 50W100

Max Oil Temp: 245⁰F

Oil Pressure

Minimum:  25 psi

Maximum: 100 psi

Load Factor

Flaps up:       +4.4g, -1.76g

Flaps down:  +3.5g