Piper Warrior

PA28-161

V-Speeds

Vso		44

Vs		50

Vx		63

Vy		79

Va		111 @ 2325 lbs

88 @ 1531 lbs

Vfe		103

Vno		126

Vne		160

Best Glide	73 KIAS

Normal Takeoff

- Rotate near 60 KIAS

Short-field takeoff

Lift off at 52 KIAS

w/ flaps 25°

Enroute Climb

87 KIAS

Normal Approach

40° Flaps 	63 KIAS

Flaps up 	70 KIAS

Balked landing

30° flaps 	63 KIAS

Max. dem. x-wind

17KIAS

Propeller	Sensenich 2 bladed fixed pitch 72”-74” diameter

Engine	Lycoming 0-320-D3G

160 Hp @ 2700 RPM and sea level.  Four cylinder, direct drive, horizontally opposed, air cooled

Fuel	100 green or 100LL blue 50 gal total 48 gal useable

25 gal each side

10 gph approximate

Electrical	14 volt DC system

14 volt 60 amp alternator

12 volt battery

Oil	8qts. Max

SAE 50 above 60°F

SAE 40 30°-90° F

SAE 30 0°- 70° F

SAE 20 below 10° F

Max. ramp weight	2325

Max. T.0. weight	2325

N9555C

Basic Empty 		1485.4

Moment		129067.583

Arm (C.G.)		86.8907924”

Useful Load		839.6

Max Takeoff Wt	2325 Lbs

Baggage max.		200 lbs.

Normal Category if over 2000 lbs.

Load Factor

Normal	3.8g-0

Utility		4.4g-0